## Slide 1
Return-Oriented Flush-Reload
Side Channels on ARM and
Their Implications for Android Devices
Xiaokuan Zhang, Yuan Xiao, Yinqian Zhang
Dept. of Computer Science & Engineering
The Ohio State University
X. Zhang, Y. Xiao, Y. Zhang

## Slide 2
Cache Side-Channel Attacks
Attacker can learn sensitive information by monitoring cache accesses made by the victim in a shared computer system
Threat model:
Physical Machine
X. Zhang, Y. Xiao, Y. Zhang

## Slide 3
  Cache Side-Channel Attacks
Prime+Probe
  work on cache sets
  attacker needs to know virtual-to-physical mapping of the victim
Flush+Reload
  work on cache lines
  attacker needs physical memory sharing with the victim
X. Zhang, Y. Xiao, Y. Zhang
Notes: ;

## Slide 4
L1 CACHE
L2 CACHE
L3 CACHE
VICTIM CORE
ATTACKER CORE
Flush-Reload Side-Channel Attack on x86
X. Zhang, Y. Xiao, Y. Zhang

## Slide 5
Flush-Reload Side-Channel Attack on x86
L1 CACHE
L2 CACHE
L3 CACHE
VICTIM CORE
ATTACKER CORE
FLUSH
(clflush)
X. Zhang, Y. Xiao, Y. Zhang

## Slide 6
L1 CACHE
L2 CACHE
L3 CACHE
ATTACKER CORE
FLUSH
(clflush)
INCLUSIVE!
VICTIM CORE
Flush-Reload Side-Channel Attack on x86
X. Zhang, Y. Xiao, Y. Zhang

## Slide 7
L1 CACHE
L2 CACHE
L3 CACHE
VICTIM CORE
ATTACKER CORE
FLUSH
(clflush)
Flush-Reload Side-Channel Attack on x86
X. Zhang, Y. Xiao, Y. Zhang

## Slide 8
L1 CACHE
L2 CACHE
L3 CACHE
VICTIM CORE
ATTACKER CORE
IDLE
Flush-Reload Side-Channel Attack on x86
X. Zhang, Y. Xiao, Y. Zhang

## Slide 9
L1 CACHE
L2 CACHE
L3 CACHE
VICTIM CORE
ATTACKER CORE
IDLE
Flush-Reload Side-Channel Attack on x86
X. Zhang, Y. Xiao, Y. Zhang

## Slide 10
L1 CACHE
L2 CACHE
L3 CACHE
VICTIM CORE
ATTACKER CORE
RELOAD&TIME
(rdtsc)
Flush-Reload Side-Channel Attack on x86
X. Zhang, Y. Xiao, Y. Zhang

## Slide 11
L1 CACHE
L2 CACHE
L3 CACHE
VICTIM CORE
ATTACKER CORE
FAST
ACCESSED
BY VICTIM
IN L3 CACHE
RELOAD&TIME
(rdtsc)
Flush-Reload Side-Channel Attack on x86
X. Zhang, Y. Xiao, Y. Zhang

## Slide 12
FLUSH-RELOAD
INTERVAL
FLUSH-RELOAD
INTERVAL
FLUSH
IDLE
FLUSH
IDLE
FLUSH-RELOAD
CYCLE
RELOAD
RELOAD
FAST  ACCESS
SLOW  NO ACCESS
Flush-Reload Side-Channel Attack on x86
X. Zhang, Y. Xiao, Y. Zhang
Notes: FLUSH: A flushes a chunk locating in a shared memory page using clflush, and it contains specific instructions.
IDLE: A waits for a pre-determined interval while B is accessing the last level cache on another CPU core.
RELOAD: A measures the time of reloading the same chunk into the cache.
If the time is shorter, it means that these instructions has been already in the cache. In other words, B has executed these instructions.

## Slide 13
Flush-Reload on ARM
“Flush-Reload is not applicable on ARM”
  --- [Yarom et al., Security’14]
X. Zhang, Y. Xiao, Y. Zhang

## Slide 14
OUTLINE
ARM Cache Exploration
Return-Oriented Flush-Reload Attacks on ARM
Case studies on Android
Conclusion
X. Zhang, Y. Xiao, Y. Zhang

## Slide 15
Challenges
 | Intel | ARM
Unprivileged Cache Flush Instruction | clflush | ???
Cache Inclusiveness | Inclusive last-level cache | ???
X. Zhang, Y. Xiao, Y. Zhang
Note: Last-level cache on ARM is L2 cache
Notes: Talk about LLC is L2 on ARM

## Slide 16
LLC Flush-Reload Requirements
Flush:
  Local L1 cache
  Shared L2 cache
  L1 cache of other cores
L2 cache:
  Victim’s memory access must put the cache line into L2 cache
X. Zhang, Y. Xiao, Y. Zhang

## Slide 17
LLC Flush-Reload Requirements
Flush:
  Local L1 cache
  Shared L2 cache
  L1 cache of other cores
L2 cache:
  Victim’s memory access must put the cache line into L2 cache
see changes in L2 cache
X. Zhang, Y. Xiao, Y. Zhang

## Slide 18
LLC Flush-Reload Requirements
Flush:
  Local L1 cache
  Shared L2 cache
  L1 cache of other cores
L2 cache:
  Victim’s memory access must put the cache line into L2 cache
X. Zhang, Y. Xiao, Y. Zhang

## Slide 19
LLC Flush-Reload Requirements: Flush(3)
L1 CACHE
L2 CACHE
VICTIM CORE
ATTACKER CORE
FLUSH
X. Zhang, Y. Xiao, Y. Zhang

## Slide 20
LLC Flush-Reload Requirements: Flush(3)
L1 CACHE
L2 CACHE
VICTIM CORE
ATTACKER CORE
FLUSH
X. Zhang, Y. Xiao, Y. Zhang

## Slide 21
LLC Flush-Reload Requirements: Flush(3)
L1 CACHE
L2 CACHE
VICTIM CORE
ATTACKER CORE
RELOAD&TIME
Memory
Access
Time
X. Zhang, Y. Xiao, Y. Zhang

## Slide 22
LLC Flush-Reload Requirements
Flush:
  Local L1 cache
  Shared L2 cache
  L1 cache of other cores
L2 cache:
  Victim’s memory access must put the cache line into L2 cache
X. Zhang, Y. Xiao, Y. Zhang

## Slide 23
LLC Flush-Reload Requirements: LLC
L1 CACHE
L2 CACHE
VICTIM CORE
ATTACKER CORE
FLUSH
X. Zhang, Y. Xiao, Y. Zhang

## Slide 24
LLC Flush-Reload Requirements: LLC
L1 CACHE
L2 CACHE
VICTIM CORE
ATTACKER CORE
FLUSH
X. Zhang, Y. Xiao, Y. Zhang

## Slide 25
LLC Flush-Reload Requirements: LLC
L1 CACHE
L2 CACHE
VICTIM CORE
ATTACKER CORE
IDLE
X. Zhang, Y. Xiao, Y. Zhang

## Slide 26
LLC Flush-Reload Requirements: LLC
L1 CACHE
L2 CACHE
VICTIM CORE
ATTACKER CORE
RELOAD&TIME
Memory
Access
Time
X. Zhang, Y. Xiao, Y. Zhang

## Slide 27
LLC Flush-Reload Requirements
Flush:
  Local L1 cache
  Shared L2 cache
  L1 cache of other cores
L2 cache:
  Victim’s memory access must put the cache line into L2 cache
X. Zhang, Y. Xiao, Y. Zhang

## Slide 28
Cache Flush Interface
Attack model: zero-permission Android app
  need to find a userspace cache flush interface
Userspace: clearcache system call
  no privilege required
  support self-modifying code
  no specification on how to implement
Need to empirically study its effect
Flushes I-cache
X. Zhang, Y. Xiao, Y. Zhang
Notes: Our attack model is that the attacker can use a zero-permission Android app to perform the attack. Therefore, we need to find a cache flush interface that we can use without any privileges.
Clearcache is a system call that is accessible by unprivileged Android
apps. ARM does not maintain cache coherence between data cache and
instruction cache. To run self-modifying code, the application itself must use clearcache system call to clear the staled code from the instruction cache after the code has been modified on the data side. Therefore, clearcache is designed to flush only the instruction cache. However, ARM specification does not specify how this system call is implemented. That is, whether flushing L1 instruction cache will also flush the shared L2 cache, which is a requirement for our attack. Therefore, we need to design novel methods to empirically determine the effect of clearcache.

## Slide 29
Cache Flush Interface: clearcache
Effect of clearcache:
  Local L1 cache?
  Shared L2 cache?
  L1 cache of other cores?
Experiment:
  Zero-permission Android app with NDK
  Two threads running on two cores
  1K dummy function (consists of “nop”)
X. Zhang, Y. Xiao, Y. Zhang

## Slide 30
L2 CACHE
Core 0
Core 1
Thread A
Thread B
A: Execute Dummy
Cache Flush Interface: clearcache
B: Idle
X. Zhang, Y. Xiao, Y. Zhang

## Slide 31
Core 0
Core 1
Thread A
Thread B
T1: L1 Access Time
Cache Flush Interface: clearcache
A: Execute Dummy
L2 CACHE
B: Idle
X. Zhang, Y. Xiao, Y. Zhang

## Slide 32
Core 0
Core 1
Thread A
Thread B
A: Cleanse L1+L2
Execute Dummy
T1: L1 Access Time
Cache Flush Interface: clearcache
L2 CACHE
B: Idle
X. Zhang, Y. Xiao, Y. Zhang

## Slide 33
B: Idle
Core 0
Core 1
Thread A
Thread B
A: Cleanse L1+L2
Execute Dummy
T1 L1 Access Time
T1: L1 Access Time
Cache Flush Interface: clearcache
L2 CACHE
X. Zhang, Y. Xiao, Y. Zhang

## Slide 34
B: Idle
Core 0
Core 1
Thread A
Thread B
A: Cleanse L1+L2
Execute Dummy
T1 L1 Access Time
T1 L1 Access Time
T1: L1 Access Time
Cache Flush Interface: clearcache
L2 CACHE
X. Zhang, Y. Xiao, Y. Zhang

## Slide 35
B: Idle
T1 L1 Access Time
T1: L1 Access Time
Core 0
Core 1
Thread A
Thread B
T4:Memory Access Time
A: Cleanse L1+L2
Execute Dummy
Cache Flush Interface: clearcache
L2 CACHE
X. Zhang, Y. Xiao, Y. Zhang

## Slide 36
B: Idle
T1 L1 Access Time
T1: L1 Access Time
T4:Memory Access Time
Core 0
Core 1
Thread A
Thread B
???
???
T2:Effects of Clearcache
On Local Core
A: Clearcache
Execute Dummy
Cache Flush Interface: clearcache
L2 CACHE
X. Zhang, Y. Xiao, Y. Zhang

## Slide 37
T1 L1 Access Time
T1: L1 Access Time
T4:Memory Access Time
T2:Effects of Clearcache
On Local Core
Core 0
Core 1
Thread A
Thread B
???
???
T3:Effects of Clearcache
On Another Core
Cache Flush Interface: clearcache
L2 CACHE
A: Execute Dummy
B: Clearcache
X. Zhang, Y. Xiao, Y. Zhang

## Slide 38
Measurement | Thread A | Thread B | PURPOSE
T1 | Execute Dummy | Idle | L1 cache access time
T2 | Clearcache, Execute Dummy | Idle | effects of clearcache on local core
T3 | Execute Dummy | Clearcache | effects of clearcache on a different core
T4 | Cleanse L1+L2, Execute Dummy | Idle | memory access time
Cache Flush Interface: clearcache
X. Zhang, Y. Xiao, Y. Zhang

## Slide 39
Measurement | Thread A | Thread B | PURPOSE
T1 | Execute Dummy | Idle | L1 cache access time
T2 | Clearcache, Execute Dummy | Idle | effects of clearcache on local core
T3 | Execute Dummy | Clearcache | effects of clearcache on a different core
T4 | Cleanse L1+L2, Execute Dummy | Idle | memory access time
Cache Flush Interface: clearcache
X. Zhang, Y. Xiao, Y. Zhang

## Slide 40
Measurement | Thread A | Thread B | PURPOSE
T1 | Execute Dummy | Idle | L1 cache access time
T2 | Clearcache, Execute Dummy | Idle | effects of clearcache on local core
T3 | Execute Dummy | Clearcache | effects of clearcache on a different core
T4 | Cleanse L1+L2, Execute Dummy | Idle | memory access time
Cache Flush Interface: clearcache
X. Zhang, Y. Xiao, Y. Zhang

## Slide 41
Measurement | Thread A | Thread B | PURPOSE
T1 | Execute Dummy | Idle | L1 cache access time
T2 | Clearcache, Execute Dummy | Idle | effects of clearcache on local core
T3 | Execute Dummy | Clearcache | effects of clearcache on a different core
T4 | Cleanse L1+L2, Execute Dummy | Idle | memory access time
Cache Flush Interface: clearcache
X. Zhang, Y. Xiao, Y. Zhang

## Slide 42
Testbed
 | Samsung Galaxy S5 | Samsung Galaxy S6 | Google Nexus 6
Number of CPUs | 2 | 2 | 1
Architecture | 32-bit ARMv7 | 64-bit ARMv8 | 32-bit ARMv7
CPU Type | Cortex-A15 Cortex-A70 | Cortex-A57 Cortex-A53 | Krait 450
X. Zhang, Y. Xiao, Y. Zhang

## Slide 43
Clearcache Experiment Result
X. Zhang, Y. Xiao, Y. Zhang

## Slide 44
Clearcache Experiment Result
X. Zhang, Y. Xiao, Y. Zhang

## Slide 45
LLC Flush-Reload Requirements
Flush:
  Local L1 cache
  Shared L2 cache
  L1 cache of other cores
L2 cache:
  Victim’s memory access must put the cache line into L2 cache
X. Zhang, Y. Xiao, Y. Zhang

## Slide 46
Cache Inclusiveness
Is L2 cache inclusive, exclusive or non-inclusive to L1 cache?
Inclusive: L1 L2
Exclusive: L1 L2 =
Non-inclusive: in between
X. Zhang, Y. Xiao, Y. Zhang

## Slide 47
Cache Inclusiveness
X. Zhang, Y. Xiao, Y. Zhang
Experiment: timing side channel
All 5 processors have inclusive L2 cache

## Slide 48
Recall: LLC Flush-Reload Requirements
Cortex A57&A53 !!!
Flush:
  Local L1 cache
  Shared L2 cache
  L1 cache of other cores
L2 cache:
  Victim’s memory access must put the cache line into L2 cache
X. Zhang, Y. Xiao, Y. Zhang
Notes: we demonstrate our attacks on S6. As they , we anticipate …
Actually, this is a general method to determine whether a processor is vulnerable to F-R attacks.

## Slide 49
OUTLINE
ARM Cache Exploration
Return-Oriented Flush-Reload Attacks on ARM
Case studies on Android
Conclusion
X. Zhang, Y. Xiao, Y. Zhang

## Slide 50
Challenges: Reload Using Instruction Cache
Can only use instruction cache reload
Have to execute an entire function
  Need to reconstruct program semantics
  Execution time of a function may vary
  Flush and Reload take too long
X. Zhang, Y. Xiao, Y. Zhang

## Slide 51
Return-Oriented Programming
Stack
Heap
Return Address 1
Return Address 2
Libraries
LOAD Gadget ret
STORE Gadget ret
Victim Program
Return Address 3
ADD Gadget ret
ATTACKER
Shared Libraries
X. Zhang, Y. Xiao, Y. Zhang

## Slide 52
Return-Oriented Reloads: Basic Idea
Android App
Shared Library
T1 = Timer();
Jump Gadget1;
Jump Gadget2;
Jump Gadget3;
T2 = Timer();
Gadget1 return
Gadget2 return
Gadget3 return
X. Zhang, Y. Xiao, Y. Zhang

## Slide 53
Return-Oriented Reloads: Basic Idea
Android App
Shared Library
T1 = Timer();
Jump Gadget1;
Jump Gadget2;
Jump Gadget3;
T2 = Timer();
Gadget1 return
Gadget2 return
Gadget3 return
X. Zhang, Y. Xiao, Y. Zhang

## Slide 54
Android App
T1 = Timer();
Jump Gadget1;
Jump Gadget2;
Jump Gadget3;
T2 = Timer();
Shared Library
Gadget1 return
Gadget2 return
Gadget3 return
Return-Oriented Reloads: Basic Idea
X. Zhang, Y. Xiao, Y. Zhang

## Slide 55
Shared Library
Gadget1 return
Gadget2 return
Gadget3 return
Android App
T1 = Timer();
Jump Gadget1;
Jump Gadget2;
Jump Gadget3;
T2 = Timer();
Return-Oriented Reloads: Basic Idea
X. Zhang, Y. Xiao, Y. Zhang

## Slide 56
Shared Library
Gadget1 return
Gadget2 return
Gadget3 return
Android App
T1 = Timer();
Jump Gadget1;
Jump Gadget2;
Jump Gadget3;
T2 = Timer();
Return-Oriented Reloads: Basic Idea
X. Zhang, Y. Xiao, Y. Zhang

## Slide 57
Shared Library
Gadget1 return
Gadget2 return
Gadget3 return
Android App
T1 = Timer();
Jump Gadget1;
Jump Gadget2;
Jump Gadget3;
T2 = Timer();
Return-Oriented Reloads: Basic Idea
X. Zhang, Y. Xiao, Y. Zhang

## Slide 58
Shared Library
Gadget1 return
Gadget2 return
Gadget3 return
Android App
T1 = Timer();
Jump Gadget1;
Jump Gadget2;
Jump Gadget3;
T2 = Timer();
Return-Oriented Reloads: Basic Idea
X. Zhang, Y. Xiao, Y. Zhang

## Slide 59
Android App
T1 = Timer();
Jump Gadget1;
Jump Gadget2;
Jump Gadget3;
T2 = Timer();
Shared Library
Gadget1 return
Gadget2 return
Gadget3 return
Return-Oriented Reloads: Basic Idea
X. Zhang, Y. Xiao, Y. Zhang

## Slide 60
Shared Library
Gadget1 return
Gadget2 return
Gadget3 return
Android App
T1 = Timer();
Jump Gadget1;
Jump Gadget2;
Jump Gadget3;
T2 = Timer();
Reload=T2-T1
Return-Oriented Reloads: Basic Idea
X. Zhang, Y. Xiao, Y. Zhang

## Slide 61
Indirect Control-flow Transfer Instructions
Architecture | Instruction | Effect
ARM v7 (32 bit) | bx lr | PC := lr
 | bx rm | PC := rm
 | blx rm | lr (r14) := next instruction PC := rm
 | mov pc, lr | PC := lr
 | pop {pc} | PC := top of stack
 | ldm {pc} | load multiple registers
X. Zhang, Y. Xiao, Y. Zhang

## Slide 62
Architecture | Instruction | Effect
ARM v8 (64 bit) | br xm | PC := xm
 | blr xm | lr (x30) := next instruction PC := xm
 | ret xm | PC := xm
 | ret | PC := lr
Indirect Control-flow Transfer Instructions
X. Zhang, Y. Xiao, Y. Zhang

## Slide 63
0x24670 <clock_gettime>
Return-Oriented Reloads: Example
Android App
libc.so
mov x19, 0x246a0
mov x20, x30
Label: adr x4, Label
add x4, x4, #12
br x19
mov x30, x20
mov x19, 0x246fc
blr x19
…
0x246a0 blr x4
0x246fc ret
X19
X. Zhang, Y. Xiao, Y. Zhang

## Slide 64
Android App
libc.so
mov x19, 0x246a0
mov x20, x30
Label: adr x4, Label
add x4, x4, #12
br x19
mov x30, x20
mov x19, 0x246fc
blr x19
…
0x24670 <clock_gettime>
0x246a0 blr x4
0x246fc ret
Return-Oriented Reloads: Example
X. Zhang, Y. Xiao, Y. Zhang

## Slide 65
Android App
libc.so
mov x19, 0x246a0
mov x20, x30
Label: adr x4, Label
add x4, x4, #12
br x19
mov x30, x20
mov x19, 0x246fc
blr x19
…
0x24670 <clock_gettime>
0x246a0 blr x4
0x246fc ret
Return-Oriented Reloads: Example
X. Zhang, Y. Xiao, Y. Zhang

## Slide 66
Android App
libc.so
mov x19, 0x246a0
mov x20, x30
Label: adr x4, Label
add x4, x4, #12
br x19
mov x30, x20
mov x19, 0x246fc
blr x19
…
0x24670 <clock_gettime>
0x246a0 blr x4
0x246fc ret
Return-Oriented Reloads: Example
X4
X. Zhang, Y. Xiao, Y. Zhang

## Slide 67
0x24670 <clock_gettime>
Android App
libc.so
mov x19, 0x246a0
mov x20, x30
Label: adr x4, Label
add x4, x4, #12
br x19
mov x30, x20
mov x19, 0x246fc
blr x19
…
0x246a0 blr x4
0x246fc ret
Return-Oriented Reloads: Example
X. Zhang, Y. Xiao, Y. Zhang

## Slide 68
0x24670 <clock_gettime>
Android App
libc.so
mov x19, 0x246a0
mov x20, x30
Label: adr x4, Label
add x4, x4, #12
br x19
mov x30, x20
mov x19, 0x246fc
blr x19
…
0x246a0 blr x4
0x246fc ret
Return-Oriented Reloads: Example
X. Zhang, Y. Xiao, Y. Zhang

## Slide 69
0x24670 <clock_gettime>
0x246a0 blr x4
0x246fc ret
Android App
libc.so
mov x19, 0x246a0
mov x20, x30
Label: adr x4, Label
add x4, x4, #12
br x19
mov x30, x20
mov x19, 0x246fc
blr x19
…
Return-Oriented Reloads: Example
X. Zhang, Y. Xiao, Y. Zhang

## Slide 70
0x24670 <clock_gettime>
0x246a0 blr x4
0x246fc ret
Android App
libc.so
mov x19, 0x246a0
mov x20, x30
Label: adr x4, Label
add x4, x4, #12
br x19
mov x30, x20
mov x19, 0x246fc
blr x19
…
Return-Oriented Reloads: Example
X. Zhang, Y. Xiao, Y. Zhang

## Slide 71
Android App
libc.so
mov x19, 0x246a0
mov x20, x30
Label: adr x4, Label
add x4, x4, #12
br x19
mov x30, x20
mov x19, 0x246fc
blr x19
…
0x24670 <clock_gettime>
0x246a0 blr x4
0x246fc ret
Return-Oriented Reloads: Example
X19
X. Zhang, Y. Xiao, Y. Zhang

## Slide 72
0x24670 <clock_gettime>
Android App
libc.so
mov x19, 0x246a0
mov x20, x30
Label: adr x4, Label
add x4, x4, #12
br x19
mov x30, x20
mov x19, 0x246fc
blr x19
…
0x246a0 blr x4
0x246fc ret
Return-Oriented Reloads: Example
X. Zhang, Y. Xiao, Y. Zhang

## Slide 73
Android App
libc.so
mov x19, 0x246a0
mov x20, x30
Label: adr x4, Label
add x4, x4, #12
br x19
mov x30, x20
mov x19, 0x246fc
blr x19
…
0x24670 <clock_gettime>
0x246a0 blr x4
0x246fc ret
Return-Oriented Reloads: Example
X. Zhang, Y. Xiao, Y. Zhang

## Slide 74
0x24670 <clock_gettime>
Android App
libc.so
mov x19, 0x246a0
mov x20, x30
Label: adr x4, Label
add x4, x4, #12
br x19
mov x30, x20
mov x19, 0x246fc
blr x19
…
0x246a0 blr x4
0x246fc ret
Return-Oriented Reloads: Example
X. Zhang, Y. Xiao, Y. Zhang

## Slide 75
Android App
libc.so
mov x19, 0x246a0
mov x20, x30
Label: adr x4, Label
add x4, x4, #12
br x19
mov x30, x20
mov x19, 0x246fc
blr x19
…
0x24670 <clock_gettime>
0x246a0 blr x4
0x246fc ret
Return-Oriented Reloads: Example
X. Zhang, Y. Xiao, Y. Zhang

## Slide 76
OUTLINE
ARM Cache Exploration
Return-Oriented Flush-Reload Attacks on ARM
Case studies on Android
Conclusion
X. Zhang, Y. Xiao, Y. Zhang

## Slide 77
Case Studies on Android
Testbed: Samsung Galaxy S6, Android 5.1.1
Two categories of attacks:
  detecting hardware events
  tracing software execution paths
--- Touchscreen
--- SurfaceFlinger
X. Zhang, Y. Xiao, Y. Zhang

## Slide 78
An Interrupt-based Touchscreen Side Channel
/proc/interrupts
[Diao et al., SP’16]
X. Zhang, Y. Xiao, Y. Zhang

## Slide 79
/proc/interrupts
Interrupt Time Series
An Interrupt-based Touchscreen Side Channel
[Diao et al., SP’16]
X. Zhang, Y. Xiao, Y. Zhang

## Slide 80
/proc/interrupts
Interrupt Time Series
Unlock Pattern
An Interrupt-based Touchscreen Side Channel
[Diao et al., SP’16]
X. Zhang, Y. Xiao, Y. Zhang

## Slide 81
/proc/interrupts
[Diao et al., SP’16]
Interrupt Time Series
Unlock Pattern
An Interrupt-based Touchscreen Side Channel
X. Zhang, Y. Xiao, Y. Zhang

## Slide 82
Partial Workflow of Android Touch Events
/dev/input/eventX
Input Event
Driver
Touchscreen Driver
Touchscreen
Hardware
Linux Kernel
EventHub
HAL
Call input_sync()
touch
Flush-Reload
X. Zhang, Y. Xiao, Y. Zhang

## Slide 83
Partial Workflow of Android Display System
Application
Surface
BufferQueue
SystemUI
Surface
BufferQueue
SurfaceFlinger
(compose buffers)
Hardware
Composer
HAL
Hardware IndependentLayer
Call postFrameBuffer()
Flush-Reload
X. Zhang, Y. Xiao, Y. Zhang

## Slide 84
Detecting Push Notifications
3s
X. Zhang, Y. Xiao, Y. Zhang
infer user’s private action
Notes: line chart
low reading

## Slide 85
Detecting Display Updates
0.5s
X. Zhang, Y. Xiao, Y. Zhang

## Slide 86
Detecting Display Updates
X. Zhang, Y. Xiao, Y. Zhang
learn inter-keystroke information

## Slide 87
Practical Considerations
  CPU frequency scaling: maximum frequency
  Power consumption: 1.5% battery per 20 min
  Library version: 64 bit vs. 32 bit
X. Zhang, Y. Xiao, Y. Zhang

## Slide 88
Countermeasures
  Disallow userspace cache flushes
  Restrict fine-grained time measurement
  Prevent physical memory sharing
X. Zhang, Y. Xiao, Y. Zhang

## Slide 89
OUTLINE
ARM Cache Exploration
Return-Oriented Flush-Reload Attacks on ARM
Case studies on Android
Conclusion
X. Zhang, Y. Xiao, Y. Zhang

## Slide 90
Conclusion
Explored clearcache system call and cache inclusiveness on ARM
Designed a novel return-oriented Flush-Reload mechanism
Showed two categories of Flush-Reload attacks on Android devices
X. Zhang, Y. Xiao, Y. Zhang

## Slide 91
Thanks for listening!
Xiaokuan Zhang
zhang.5840@osu.edu
X. Zhang, Y. Xiao, Y. Zhang

## Slide 93
LLC Flush-Reload Requirements: Flush(1)
L1 CACHE
L2 CACHE
VICTIM CORE
ATTACKER CORE
FLUSH

## Slide 94
LLC Flush-Reload Requirements: Flush(1)
L1 CACHE
L2 CACHE
VICTIM CORE
ATTACKER CORE
RELOAD&TIME

## Slide 95
LLC Flush-Reload Requirements: Flush(2)
L1 CACHE
L2 CACHE
VICTIM CORE
ATTACKER CORE
FLUSH

## Slide 96
LLC Flush-Reload Requirements: Flush(2)
L1 CACHE
L2 CACHE
VICTIM CORE
ATTACKER CORE
FLUSH

## Slide 97
LLC Flush-Reload Requirements: Flush(2)
L1 CACHE
L2 CACHE
VICTIM CORE
ATTACKER CORE
RELOAD&TIME

## Slide 98
Experiment setup: Android App with NDK
One thread, 1K dummy function
X. Zhang, Y, Xiao, Y. Zhang
Cache Inclusiveness

## Slide 99
Cache Inclusiveness --- Instruction Cache
L2 CACHE
L1-I
L1-D
Execute Dummy
X. Zhang, Y, Xiao, Y. Zhang
L1 CACHE

## Slide 100
L2 CACHE
L1-I
L1-D
T1: L1 Access Time
Execute Dummy
X. Zhang, Y, Xiao, Y. Zhang
Cache Inclusiveness --- Instruction Cache
T1: L1 Access Time
T1: L1 Access Time
L1 CACHE

## Slide 101
L2 CACHE
L1-I
L1-D
T1: L1 Access Time
X. Zhang, Y, Xiao, Y. Zhang
Cache Inclusiveness --- Instruction Cache
T1: L1 Access Time
T1: L1 Access Time
L1 CACHE
Cleanse L2
Execute Dummy

## Slide 102
L2 CACHE
L1-I
L1-D
T1: L1 Access Time
X. Zhang, Y, Xiao, Y. Zhang
Cache Inclusiveness --- Instruction Cache
T1: L1 Access Time
T1: L1 Access Time
L1 CACHE
Cleanse L2
Execute Dummy

## Slide 103
L2 CACHE
L1-I
L1-D
L2 Inclusive to L1-I?
YES/NO
T1: L1 Access Time
X. Zhang, Y, Xiao, Y. Zhang
Cache Inclusiveness --- Instruction Cache
T1: L1 Access Time
T1: L1 Access Time
L1 CACHE
Cleanse L2
Execute Dummy

## Slide 104
L2 CACHE
L1-I
L1-D
T1: L1 Access Time
X. Zhang, Y, Xiao, Y. Zhang
Cache Inclusiveness --- Instruction Cache
T1: L1 Access Time
T1: L1 Access Time
L2 Inclusive to L1-I?
YES
L1 CACHE
Cleanse L2
Execute Dummy

## Slide 105
L2 CACHE
L1-I
L1-D
X. Zhang, Y, Xiao, Y. Zhang
Cache Inclusiveness --- Instruction Cache
T1: L1 Access Time
T1: L1 Access Time
T1: L1 Access Time
L2 Inclusive to L1-I?
YES
L1 CACHE
Cleanse L2
Execute Dummy

## Slide 106
L2 CACHE
L1-I
L1-D
X. Zhang, Y, Xiao, Y. Zhang
Cache Inclusiveness --- Instruction Cache
T1: L1 Access Time
T1: L1 Access Time
T1: L1 Access Time
L2 Inclusive to L1-I?
YES
L1 CACHE
Cleanse L2
Execute Dummy

## Slide 107
L2 CACHE
L1-I
L1-D
T2: Mem Access Time
X. Zhang, Y, Xiao, Y. Zhang
Cache Inclusiveness --- Instruction Cache
T1: L1 Access Time
L2 Inclusive to L1-I?
YES
L1 CACHE
Cleanse L2
Execute Dummy

## Slide 108
L2 CACHE
L1-I
L1-D
T1: L1 Access Time
X. Zhang, Y, Xiao, Y. Zhang
Cache Inclusiveness --- Instruction Cache
T1: L1 Access Time
L2 Inclusive to L1-I?
NO
L1 CACHE
Cleanse L2
Execute Dummy

## Slide 109
L2 CACHE
L1-I
L1-D
T1: L1 Access Time
X. Zhang, Y, Xiao, Y. Zhang
Cache Inclusiveness --- Instruction Cache
T1: L1 Access Time
L2 Inclusive to L1-I?
NO
L1 CACHE
Cleanse L2
Execute Dummy

## Slide 110
L2 CACHE
L1-I
L1-D
T2: L1 Access Time
T1: L1 Access Time
X. Zhang, Y, Xiao, Y. Zhang
Cache Inclusiveness --- Instruction Cache
T2: L1 Access Time
T1: L1 Access Time
T2: Mem Access Time
L2 Inclusive to L1-I?
NO
L1 CACHE
Cleanse L2
Execute Dummy

## Slide 111
Cache Inclusiveness
Smartphone |  | T1 | T2 | Inclusiveness
Krait 450 | D-cache | 1169 | 3700 | inclusive
 | I-cache | 1020 | 4350 | inclusive
Cortex-A15 | D-cache | 2600 | 6469 | inclusive
 | I-cache | 2484 | 5474 | inclusive
Cortex-A7 | D-cache | 3378 | 15460 | inclusive
 | I-cache | 3551 | 15822 | inclusive
Cortex-A57 | D-cache | 223 | 907 | inclusive
 | I-cache | 150 | 794 | inclusive
Cortex-A53 | D-cache | 325 | 1633 | inclusive
 | I-cache | 275 | 1287 | inclusive
X. Zhang, Y. Xiao, Y. Zhang